## Slide 1: Counter
Digital electronics

## Slide 2: Introduction to counter
A counter is a sequential digital device, which stores (or sometimes displays)the number of times a particular event or process has occurred.
Counters is a very wide application of flip-flops, where it is a group of flip-flops with a clock signal applied .

## Slide 3: Types of counters :
Synchronous counters
Asynchronous counters

## Slide 4: Difference between synchronous and asynchronous counter
Synchronous counter | Asynchronous counter
Only 1 clock pulse is common for all flip flop | each flip flop output serves as the clock input signal for the next FF in the sequence
It is a random counter | It is a sequential counter, which uses up counter or down counter
It is a faster then asynchronous counter | It is slower
Extra circuits requires | Less circuits required
Complex design | Simple design
Cost high | Cost low

## Slide 5: Cont.
Synchronous counter | Asynchronous counter
Less delay | More delay
Ex. Ring counter, johnson counter | Ex. Ripple counter

## Slide 6: Questions
How to find the Mod value of counter?
Different states
mod
After 21 clock pulse ,which state will come?
How to find no of flip flops required to design Mod –n counter?
2n≥ N or log 2N

## Slide 7: More uses of counter
It is used to count the no. of pulses.
It can be used as frequency divider circuit
An n bit counter will have 2n state

## Slide 8: Applications
Digital clock
Frequency counter
Analog to digital converter

## Slide 9: Designing of asynchronous counter
Decide the no. of flip flops
Type of flip flop
Truth table of counter
Obtain simplified equation using k-map
Draw the logic diagram

## Slide 10: Design the BCD ripple counter

## Slide 11: Truth table of counter

## Slide 14: Designing of synchronous counter
Decide the no. of flip flops
Type of flip flop
Truth table/Excitation table of counter
Obtain simplified equation using k-map
Draw the logic diagram

## Slide 15: Design a mod-5 synchronous counter using jk flip flop

## Slide 16: Excitation table of jk flip flop
Q | J | K | Q next
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
Q | Q next | J | K
0 | 0 | 0 | *
0 | 1 | 1 | *
1 | 0 | * | 1
1 | 1 | * | 0

## Slide 17: Truth table
Q | Q next | J | K
0 | 0 | 0 | *
0 | 1 | 1 | *
1 | 0 | * | 1
1 | 1 | * | 0

## Slide 21: Design of 3 bit synchronous up counter

## Slide 22: Design of 3 bit synchronous down counter

## Slide 23: Thank you